## Slide 1
Force on current-carrying conductor
Principles of electrical science

## Slide 2
Force on current-carrying conductor

## Slide 3
Changing direction of current
Force on current-carrying conductor

## Slide 4
Changing direction of flux
Force on current-carrying conductor

## Slide 5
F=B.I.L
where: | F | = | Mechanical force exerted on the conductor, measured in Newtons (N)
 | B | = | Flux density of main magnetic field measured in Wb ⁄ m2 – teslas (T)
 | I | = | Current flowing in conductor measured in amperes (I)
 | L | = | Length of conductor in the magnetic field measured in metres (m)
Force on current-carrying conductor

## Slide 6
Example 1
A conductor of 20cm in length is situated perpendicularly in a magnetic field of flux density of 5 teslas and has a current of 10A flowing through it. Calculate the force on the conductor.
F | = | B.I.L.
 | = | 5 × 10 × 0.2
 | = | 10 Newtons
Force on current-carrying conductor

## Slide 7
F | = | B.I.L.
 | = | 10 × 15 × 0.5
 | = | 75 Newtons
Force on current-carrying conductor
Example 2
A conductor of 0.5m in length is situated perpendicularly in a magnetic field of flux density of 10 teslas and has a current of 15A flowing through it. Calculate the force on the conductor.

## Slide 8
Fleming’s left hand motor rule
Direction of motion
Field
Current
Force on current-carrying conductor

## Slide 9
The end
Principles of electrical science